## Slide 1: Data preparation: surrogate modeling of drainage networks under coastal flooding
Mohammad Movahhed
AI for Urban Water Networks
Instructor: Dr. Fan

## Slide 2: Recap
Efficiency
Accuracy
Physics-based modeling
Surrogate modeling
Emerging Alternative
Notes: SMs are mathematical approximations employed to emulate a system’s behavior by learning the relationships between input parameters and output responses directly from precomputed simulations.

## Slide 3
Surrogate modeling
Recap
Notes: GNNs are ideal for this task since they are designed to process data over graphs by using the intrinsic structure of the network and the relations between network components.
Instead of connecting all the available features like a fully connected NN, a GNN focuses on the relationships and the corresponding parameters indicated by the graph they are representing.

## Slide 4
Required Data
Surrogate model
Storm surge
Topography
Flood model
Drainage network
SWMM model
Inundation time series
Network performance
New Storm
Estimated performance
Notes: Inundation time series & Drainage network (pipes, conduits, manholes, inlets, and outfalls)

## Slide 5
Real Case Study
10-meter DEM (USGS database )
Chart: Time (min)
Storm surge hydrograph (CHS database)
Notes: Economically significant
Densely populated
In danger of hurricanes
Coastal Hazards System (CHS)

## Slide 6
Drainage network
Flood inundation simulation
Observation point
Inundation depth (m)
0
5.5
Legend
WWTP
Outfall
Missing pipe and manhole data
Simulation took 2.83 wall-clock hours
Real Case Study

## Slide 7
Bellinge, Denmark
Covers 1.7 km2 area.
Number of manholes: 995
Number of conduits: 1015
Number of outfalls: 9
Hypothetical Case Study

## Slide 8
River is assumed to be the coastline.
Flood inundation obtained following “bathtub” models and CHS database.
Hypothetical Case Study
Chart: Time (hrs)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34
Water Elevation | 0 | 4.4444 | 6.6667 | 5.5556 | 8.8889 | 12.2222 | 11.1111 | 7.7778 | 6.6667 | 10 | 13.3333 | 15.5556 | 13.3333 | 8.8889 | 5.5556 | 7.7778 | 3.3333 | 0

## Slide 9
Hypothetical Case Study
Water depth time series at location of nodes
SWMM Network model
Inundation time series
Inundation depth (m)
0
10
Outfalls

## Slide 10
SWMM Network model
Next Steps
Simulate SWMM for all flood scenarios
Construct the GNN
Train the GNN based on SWMM

## Slide 11: Thank you for your attention