## Slide 1: Final Presentation: surrogate modeling of drainage networks under coastal flooding
Mohammad Movahhed
AI for Urban Water Networks
Instructor: Dr. Fan

## Slide 2: Recap
Efficiency
Accuracy
Physics-based modeling
Surrogate modeling
Notes: SMs are mathematical approximations employed to emulate a system’s behavior by learning the relationships between input parameters and output responses directly from precomputed simulations.

## Slide 3
Required Data
Surrogate model
Storm surge
Topography
Bathtub model
Drainage network
SWMM model
Inundation time series
Outfall discharge
New Storm
Estimated discharge

## Slide 4
Bellinge, Denmark
Consists of combined and separate systems
Over 10,000 nodes
Benchmark Case Study

## Slide 5
Combined network
1020 Nodes
1026 Edges
Benchmark Case Study
Notes: Nodes are outfalls, manholes, and storages
Links are conduits, pumps, and orifices

## Slide 6
Benchmark Case Study
Average node degree: 2.01
Average betweenness centrality: 0.0025
Assortativity coefficient: 0.0116
Triadic closure: 0.023
Network diameter cannot be defined
Notes: Average node degree: 2.01
Average betweenness centrality: 0.0025
Degree assortativity coefficient: 0.0116 (no patterns)
Triadic closure: 0.023 (no closed triads)
Network diameter cannot be defined

## Slide 7
74 storm surge scenarios with 15 min interval were gathered from the coastal hazard system data base.
Flood Scenarios
Chart: Time (hr)
Notes: River is assumed to be the coastline.

## Slide 8
74 flood scenarios following “bathtub” model and converted to rainfall depth series with 5 min intervals.
Conversion to Rainfall Scenarios
Chart: Time (hr)

## Slide 9
Discharge time series at 9 outfalls of the network were obtained from SWMM simulations for all 74 scenarios.
Drainage simulations
SWMM model
Chart: Time (hr)
Notes: Outfall discharges are just shown for one scenario

## Slide 10
GCN Structure
F74F360
G60K220
G60U02F
G70U01F
G71U02F
G71U10F
G72U07R
G75U03F
G80U03F
Three graph convolutional layers followed by ReLU
  GCN layers: 48 neurons
One fully connected layer followed by sigmoid

## Slide 11
GCN Informations
Node features as Input
Static | Dynamic
Elevation | Rainfall Past 24 timesteps (2 hours)
Depth | Time encoding Normalized timestep
X coordinate | 
Y coordinate | 
Distance to shoreline | 
SUM = | 30 features
Output: Discharge at 9 Outfalls for the current time step
Training dataset: 54 scenarios
Testing dataset: 20 scenarios

## Slide 12
Model Training
Loss function: Mean Square Error (MSE)
(Average loss of all 9 outfalls)
Optimizer: Adam optimizer with learning rate of 0.0001

## Slide 13
Model Testing
F74F360 MSE = 0.003216
G60K220 MSE = 0.003539
G60U02F MSE = 0.003308
G70U01F MSE = 0.003398
G71U02F MSE = 0.004121
G71U10F MSE = 0.003518
G72U07R MSE = 0.019106
G75U03F MSE = 0.035731
G80U03F MSE = 0.018427

## Slide 14
Conclusion
Results show that
The GCN-based surrogate model was able to provide rapid estimations with high accuracy.
Loss value converges very fast, indicating that the learning process is trivial. This might be due to poor scenario selection.
As the next step:
Select more diverse scenarios for training and testing to obtain better generalization.
Add another GCN layer to consider the relationship of neighboring nodes at a higher order
Employ a batching algorithm to improve training speed and convergence rate.
Using a higher learning rate but with reduction on plateau

## Slide 15: Thank you for your attention